## Slide 1
MODULE 6 Needle Dislodgement
Needle Dislodgement
Notes: <number>
For this reason preventing patient falls is key to keeping kidney patients safe.

## Slide 2: Preventing Venous Needle Dislodgement Is Key to Keeping Kidney Patients Safe
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 3: Venous Needle Dislodgement (VND) What is it?
A complication of hemodialysis. Ranges from minor blood loss to exsanguination (bleeding to death).
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 4: Venous Needle Dislodgement (VND) What causes it?
VND occurs when the needle delivering the cleansed blood from the machine back into the patient either partially or completely comes out of the access site. Instead of the blood being pumped back into the patient’s bloodstream, it flows onto the bed, chair and even the floor.
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 5: Facts about VND
  About 414 episodes of VND annually
  Mortality range estimated between 10-33% percent
  The number of fatal incidents in the United States may be between 40 and 136
  In dialysis population of 350,0001
  1. Sandroni, Stephen , MD, Terry Sherockman, RN, MS, and Kathy Hays-Leight RN, Allegheny General Hospital, Pittsburgh. Presented at ASN/Renal Week, Philadelphia, US, November 2008.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 6: Facts about VND
  The most likely time for a VND incident is the last two hours of dialysis. The patient may become restless and inadvertently pull out the needle.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 7: Consequences of VND
  Patients who lose more than 40% of their blood are more likely to suffer from permanent life-altering consequences such as stroke, and other permanent disabilities.
  Instances of VND can be expensive, requiring emergency care, hospitalization.
Note: Disconnection from a catheter line has the same implications as VND.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 8: Facts about VND
  In less than 7.5 minutes an average-size man receiving dialysis treatment can lose more than 50% of his blood volume from an undetected VND.
  An average-size woman can lose more than 40% of her blood volume in less than 5 minutes.
  It is considered a Class IV Hemorrhage, and it can be fatal without a rapid response.2
MODULE 6 Needle Dislodgement
2. The Human Body - How Much Blood Is In the Average Human Body? http://www.enotes.com/science-fact-finder/human-body/how-much-blood-average-human-body
Notes: <number>
<number>

## Slide 9: Risk Factors
  The VA National Center for Patient Safety found two major risk factors for bleeding during dialysis:
  75% of the most severe bleeds occurred in patients who were restless, confused, agitated, or uncooperative.
  12.5% occurred in patients who were asleep.
  In 50% of the severe bleeds, the access site was not visible at the time of the event, and in the remaining 50%, the visibility of the access site was not documented in the root cause analysis.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 10: Risk Factors
  Patient Factors:
  Patients who are mentally, cognitively, neurological impaired, such as those with dementia
  Patients who are uncooperative, agitated or restless
  Patients with frequent blood pressure drops or muscle cramps
  Patients with skin conditions, e.g., allergies to patches, eczemas, extensive sweating
  Patients with diabetes and frequent hypoglycemic episodes during HD therapy
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 11: Risk Factors
  Access Factors:
  Patients with accesses in locations which are not readily visible or easily secured (e.g., other than brachial or cephalic arteriovenous access).
  Patients whose access is covered during dialysis.
  Patients with extensive hair growth around the access points which makes fixation of the needles more difficult.
  Patient with known small blood leakage oozing around venous needle.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 12: Preventing VND
  Visually monitoring the status of the needle insertion site and blood lines is the first line of defense in detecting VND.
  The access site should remain uncovered allowing for easy visual inspection.
  The tightness of connection of blood lines to needles and catheters should be verified at the start of treatment and periodically reassessed throughout the treatment.
  Patients who are confused/agitated should be as close to the nurse’s station as possible to make it easier to monitor them.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 13: Preventing VND
  The needle should be taped securely. All staff should use the same taping technique, such as a butterfly or chevron pattern, as well as the same materials, where possible.
  Use of standard taping procedure makes it easier for staff to identify insecure initial fixation and any movement of the tape during dialysis.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 14: Preventing VND
  Blood lines should be anchored to the patient and not the chair or bed. This reduces the chance that the lines could be pulled on hard enough to dislodge the needle.
Blood lines should be looped loosely to allow
movement of the patient and to prevent blood lines pulling on the needles
MODULE 6 Needle Dislodgement
Notes: <number>
Factors contributing to patient falls are many and varied; however, 40 percent of patients who fell reported that dizziness was the main reason for their fall.
Tripping slipping and other environmental factors along with loss of balance and general weakness are also major contributors
Once a patient falls for the first time, a downward spiral leading to more falls can develop due to the patient becoming over-cautious. They may decrease physical activities for fear of fall, which weakens physical functioning and increases the likelihood of future falls.

## Slide 15: Preventing VND
  Setting the venous pressure alarm be set as close as possible to the current venous pressure, and setting it “asymmetrically.” [For example: -30 and +70 mm Hg] will reduce the number of false alarms related to movement.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 16: Preventing VND
  Smaller-gauge needles may increase risk, as they create significant flow resistance, producing back pressures that greatly exceed the patient’s venous pressure.
  As a result, the venous pressure monitor is likely to continue sensing the pressure created by the needle’s flow resistance even if the needle is dislodged from the patient.4
  4. Undetected Venous Needle Dislodgement during Hemodialysis. Hazard [Health Devices November 1998; (11):404-61. http://www.mdsr.ecri.org/summary/detail.aspx?doc_id=8300
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 17: Engage Patients and Caregivers
  Staff, patients and care givers all should be aware of VND and the consequences.
  Clear policies and procedures should be developed regarding access sites.
  All patients should be assessed for their level of risk of VND, and if appropriate, an alarm device intended for monitoring venous needle dislodgement should be used.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 18: Additional Tools for Preventing VND
  An optical sensor may be used to detect bleeding. The alarm reacts to the first drop of blood with an audible alarm and a flashing red lamp on the alarm unit.
  Enuresis pads have been used to detect blood loss from the access site by positioning the moisture detector close to the venous needle or between the two needle sites. This is not an FDA approved use of these devices
  HemaClip® patient connector clips may be used to decrease the possibility of loosening or disconnection of the return blood line at the dialysis catheter.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 19: Recommendations
  Inform dialysis staff that secure needle placement is crucial to avoiding dislodgments. Take the time to securely tape the needle to the patient's skin, arm, or access device.
  Alert dialysis staff to the dangers associated with relying on the venous pressure alarm to detect a venous line needle dislodgment. Advise them to continually examine hemodialysis blood lines during treatment if this is not already routine.
  Instruct users to keep the entire venous line from being covered by anything that might prevent good visualization of the needle insertion so that it can be easily monitored.
  Encourage users to continue to use the venous pressure monitor. While the monitor may not be able to detect a dislodged needle, it is useful for detecting obstructions or disconnections that occur elsewhere in the venous line. Instruct users to ensure that the monitor's alarm limits are set to clinically appropriate levels.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 20: Developing Policies and Procedures
Review current policies and procedures to ensure they meet current recommendations for preventing VND
Consider using a process analysis fishbone or other root cause analysis to examine policies and procedures.
Review CMS Conditions for Coverage for ESRD Facilities, section 494.110 – Medical Injuries and Medical Errors Identification.
Review examples of Quality Assessment and Performance Improvement (QAPI) projects and develop QAPI projects appropriate for your facility.
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 21: Standardized Systems
Standardized systems reduce opportunities for error.
Human errors can be caused by an individual’s short-term memory, judgment impacted by long hours, or problem solving during a stressful event.
Standardizing processes and systems minimizes the possibility for errors due to the human limitations that even the most vigilant professional can have.
Standardized systems will give staff the strength to decrease variation in patient care and, ultimately, improve safety.
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 22: System for Reporting Errors/Adverse Events
All staff—clinical, clerical, housekeeping, and maintenance—as well as patients, need specific, written directions on how to report errors or adverse events.
There should be discussions to ensure that all team members clearly know what staff is responsible for responding to errors and near misses immediately.
A reporting form should be created for documentation.
MODULE 6 Needle Dislodgement
Notes: <number>
For this reason, new staff should be immediately trained in all Fall Risk Assessment Procedures and Fall Prevention Policies.
Subsequent fall prevention training should be provided to staff during in-service training and as the need arises.
Established fall prevention policies should be reinforced through newsletter articles, brochures and other publications and by posting reminders such as posters on dialysis center bulletin boards.
Patients and caregivers should also be given every opportunity to learn more about their treatment and fall prevention strategies.

## Slide 23: Root Cause Analyses
Once a continuing or evolving problem is identified through data tracking, the facility should conduct a root cause analysis to determine contributing factors, including a review of systems that were in place and determining if processes were followed.
If not, there should be focus on staff training to prevent similar adverse events.
If processes were followed but did not ensure patient safety, the Patient Safety Officer and other key staff should identify risks that could lead to further incidents and create solutions to prevent future errors that could lead to patient injury.
MODULE 6 Needle Dislodgement
Notes: <number>
<number>

## Slide 24
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 25: Which of the following should done prior to starting a patient’s dialysis treatment?
The access should be taped securely
The access should be uncovered
The blood lines should be looped loosely
The patient should be assessed for risk of VND
All of the above
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 26: Which of the following should done prior to starting a patient’s dialysis treatment?
The access should be taped securely
The access should be uncovered
The blood lines should be looped loosely
The patient should be assessed for risk of VND
All of the above
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 27: Who is at high risk for VND?
Patients with skin conditions
Patients with dementia
Patients with frequent blood pressure drops
Patients with covered accesses
All of the above
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 28: Who is at high risk for VND?
Patients with skin conditions
Patients with dementia
Patients with frequent blood pressure drops
Patients with covered accesses
All of the above
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 29: True or False:
Blood lines should be anchored to the chair or bed to reduce the risk of VND.
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 30: True or False:
Blood lines should be anchored to the chair or bed to reduce the risk of VND.
FALSE
Blood lines should be anchored to the patient.
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 31: Additional Resources About Preventing VND
Keeping Kidney Patients Safe
http://www.kidneypatientsafety.org
Health and Safety Survey to Improve Patient Safety in End Stage Renal Disease http://www.kidneypatientsafety.org/pdf/healthsafetysurveyreports/HSSProfessionalSurveyReport_FNL_3-21-07.pdf
MODULE 6 Needle Dislodgement
Notes: <number>

## Slide 32: Additional Resources About Preventing VND
The VA National Center for Patient Safety
http://www.patientsafety.gov/alerts/BleedingEpisodesDuringDialysisAD09-02.pdf
Venous Needle Dislodgement: How to Minimize the Risks
http://www.edtnaerca.org/pdf/home/VNDpaper.pdf
European Dialysis and Transplant Nurses Association/European Renal Care Association http://www.edtnaerca.org/pages/erb/venousneedle.php
MODULE 6 Needle Dislodgement
Notes: <number>